## Slide 1: 15th GMU Conference on Atmospheric Transport and Dispersion Fairfax, VA 12-14 July 2011 HPAC Urban Model Validation Comparison of Madison Square Garden 2005 Experiments with latest HPAC Builds 99, 125 Daniel Nakada dnakada@ida.org Nathan Platt nplatt@ida.org

## Slide 2: Background
This briefing presents a comparison of field trial data with predictions from recent HPAC Releases – Build 99 and Build 125 (Maintenance Build) – within an urban environment (Madison Square Garden 2005 experiments). We compared predictions with observations using a Measure of Effectiveness (MOE) that compares the “hazardous” region above a concentration threshold of interest.
Steve Hanna (Sage Management) et al. provided the HPAC project file inputs used in this analysis.

## Slide 3
Imagery Source: U.S. Geological Survey
~1-km-by-1-km Area in Midtown Manhattan
6 Perfluorocarbon Tracers simultaneously released at 5 sites
26 Perfluorocarbon Tracer samplers
Intensive Operating Period 1 | Intensive Operating Period 2
March 10, 2005 Rel 1: 0900 – 1100 Rel 2: 1130 – 1330 | March 14, 2005 Rel 1: 0900 – 1100 Rel 2: 1130 – 1330
Midtown
Manhattan
Hudson River
MSG 2005 Field Study

## Slide 4
400m arc
(Far)
200m arc
(Near)
oc-PDCH
PMCP
PMCH, i-PPCH
PECH
1PTCH
Imagery Source: U.S. Geological Survey
MSG 2005 Field Study
Intensive Operating Period 1
Midtown
Manhattan
Hudson River

## Slide 5: HPAC Comparison Approach
HPAC simulations used 1 sec time step; concentrations were averaged over 30 minutes with background concentration levels added
Used 5 Perfluorocarbon Tracers with sufficient data
To be included in the quantitative evaluation, a data pair must have either the predicted concentration or observed concentration exceed a threshold concentration
For a brief look, 2 Meteorological Input Options / 2 Urban Model Options were examined:
Meteorological Input Options | HPAC Urban Model Options
Single (SNG) – Wind speed and direction at rooftop, averaged over several sites | UC – Urban Canopy in SCIPUFF
MEDOC (MED) – MM5 MEDOC outputs using 4 km resolution runs | UDM – Urban Dispersion Model

## Slide 6: Measure of Effectiveness
Determine threshold T exceedance quantities for each Tracer Gas and Release Period, then grouped by Regime (Near, Far and All Surface).
MOE yields up to 20 data points (5 Gases x 4 Releases) for each of 3 Regimes (Near, Far, ALL).

## Slide 7
HPAC Contour /
MOE Comparisons
Single Wind / | UDM
MEDOC / | UC

## Slide 8: HPAC 5 Contour Comparisons Example: MSG 2005 IOP1 Release 1 of PMCH – SNG / UDM
HPAC Build 99
PMCH (30min after release)
HPAC MB
PMCH (30min after release)
10-8
10-9
10-10
10-11
10-12
10-13

## Slide 9: Comparison with Tracer Data IOP1 / IOP 2 –SNG / UDM
HPAC 99
PMCH – after 30 minutes (IOP1 Release 1)
HPAC MB
PMCH – after 30 minutes (IOP1 Release 1)
Sampler
Release Location
FALSE NEGATIVE
FALSE POSITIVE
OVERLAP
Note: Logarithmic Scale is shown for Concentration

## Slide 10: Comparison with Tracer Data IOP1 / IOP 2 –SNG / UDM
HPAC Build 99
HPAC MB
Decreasing False Positive
Decreasing False Positive
Decreasing False Negative
HPAC MB
Lower Threshold
Higher Threshold
Decreasing False Negative
HPAC 99
UDM: HPAC 99 shows better performance for hazard area estimation than HPAC MB

## Slide 11: HPAC 5 Contour Comparisons Example: MSG 2005 IOP1 Release 1 of PMCH – MEDOC / UC
10-8
10-9
10-10
10-11
10-12
10-13
HPAC Build 99
PMCH (30min after release)
HPAC MB
PMCH (30min after release)
HPAC 99: MEDOC winds were used as read from the file
HPAC MB: MEDOC winds reset within the canopy.

## Slide 12: Comparison with Tracer Data IOP1 / IOP 2 –MEDOC / UC
HPAC 99
PMCH – after 30 minutes (IOP1 Release 1)
Sampler
Release Location
FALSE NEGATIVE
FALSE POSITIVE
OVERLAP
HPAC MB
PMCH – after 30 minutes (IOP1 Release 1)
Note: Logarithmic Scale is shown for Concentration

## Slide 13: Comparison with Tracer Data IOP1 / IOP 2 –MEDOC / UC
Decreasing False Positive
Decreasing False Positive
Decreasing False Negative
Lower Threshold
Higher Threshold
Decreasing False Negative
HPAC Build 99
HPAC MB
HPAC MB
HPAC 99
MEDOC: HPAC 99 predicts more false negatives while HPAC MB predicts more false positives.

## Slide 14: Conclusions
UDM – HPAC 99 shows better performance for hazard area estimation than HPAC MB - HPAC MB increases the number of false positives for lower threshold analyses and both false negatives and false positives for higher threshold analyses.
MEDOC – Generally produces wider plumes in HPAC MB, therefore predicting more false positives. Plumes in HPAC 99 tend to be narrower, predicting more false negatives.

## Slide 15
Backup

## Slide 16: Comparison with Tracer Data Average Concentration Based MOE Calculations IOP1 / IOP 2
Decreasing False Positive
Decreasing False Positive
Decreasing False Negative
SNG - UDM
MEDOC - UC
Decreasing False Negative
HPAC Build 99
HPAC MB
HPAC MB
HPAC 99