## Slide 1: Assessment of the atmospheric release induced by the Fukushima nuclear power plant accident
O.SAUNIER, A.MATHIEU, D.DIDIER, M.TOMBETTE, D.QUELO, M.BOCQUET, V.WINIAREK
Anne.mathieu@irsn.fr
Presentation of the method and validation of the source term by using model to data comparisons

## Slide 2: Operational response to the Fukushima crisis
The Fukushima crisis
  Activation of the Technical Emergency Centre for 6 weeks (24/7 – 100 p)
  Local response: Projection of a technical adviser at the French Embassy
Task
  Evaluation of the reactors state, releases (diagnostic/prognosis)
  Evaluation of the radiological consequences (doses et depositions)
  Analysis of the measures over the world
Role of IRSN in case of a Radiological Emergency
  Assess risk induced by accidental situation
  Provide technical expertise to French public Authorities
Providing a relevant technical information to the media and French people in Japan
The strong uncertainties prevent to have a complete understanding of the nuclear accident
To improve the estimate of the source term: Inverse modelling approach Source term : time evolution of the release rate and its distribution between radioisotopes

## Slide 3: Outline
Ingredients of the reconstruction
Reconstruction of the Fukushima Daiichi source term
Conclusions
Gamma dose rate observations

## Slide 4: Ingredients of the reconstruction: observations
4
Fukushima Daiichi NPP
Air concentration
Dose rate
Inverse modelling approach:
the novelty of the presented method is the use of dose rate observations
Observations | + | -
Air concentration | Easy to use (Model parameter & Isotopic composition) | Number & frequency (Very few data & Time integrated)
Deposition | Easy to use (Model parameter & Isotopic composition) | Number & frequency (Very few data during the release & Time integrated)
Dose rate | Number & Frequency | Difficult to use (Not a model parameter & Aggregate all the gamma radiations emitted by any radionuclides present on the ground and in the air)
Observations | + | -
Air concentration | Easy to use (Model parameter & Isotopic composition) | Number & frequency (Very few data & Time integrated)
Deposition | Easy to use (Model parameter & Isotopic composition) | Number & frequency (Very few data during the release & Time integrated)
Dose rate | Number & Frequency | Difficult to use (Not a model parameter & Aggregate all the gamma radiations emitted by any radionuclides present on the ground and in the air)

## Slide 5
5
Gamma dose rate observations
Information contained in the dose rate signal :
  Plume detection when it blew over the station: timing of the release events
  The slope due to the radioactive decay of the deposit: information on the isotopic composition
  The value of the observed dose rate: quantities released
Ingredients of the reconstruction: the observations

## Slide 6: Ingredients of the reconstruction: the inverse problem
The physical model for the tracers (radionuclides) can be formalized by
The objective is to assess the source term σ so that the error ε is minimized.
Cost function (minimized by using L-BFGS-B algorithm)
Requirement
  Number of observations >> Number of unknowns
Hypothesis
  No prior knowledge of the source term (σb = 0)
  Model and observations are supposed to be perfect (R = B = I)
6
Vector of observations
Estimator of the source term
Source receptor matrix
computed with the forward or adjoint model + observation operator
Vector of errors

## Slide 7
7
Ingredients of the reconstruction: the model
Dispersion model : Eulerian model ldX from the operational C3X platform
ldX Simplest reasonable numerical scheme
  Dry deposition: vdep = 2 10-3 cm/s
  Wet deposition: Λs = apob, with a = 5 10-5 and b = 1
  Vertical diffusion: Troen and Mahrt scheme
  Radioactive decay + filiation
Met. data: ECMWF (0.125°)
Spatial resolution: 0.125° x 0.125°
Consequences model : consX from C3X
Dose rate estimations
Observations
ldX simulations

## Slide 8
8
Ingredients of the reconstruction: Fukushima
The Fukushima case
Measurements: dose rate signal
  The observed signal is mainly due to the contribution of Cs-134, Cs-137, Ba-137m, I-131, I-132, Te-132, Xe-133
  ~30 dose rate stations are considered
  between the 11th and the 26th of March 11430 measurements
Source term assessment for the 7 main isotopes
    Cs-134 + Cs-137 + Ba-137m
    I-131
    I-132 + Te-132
    Xe-133
from the 11/03 till the 26/03: 7 isotopes x 380 time steps = 2660 unknowns
Insufficient number of observations: reduce the number of unknowns
Notes: 8

## Slide 9
Designed approach:
  Several steps :
      Inverse modelling to retrieve the timing of the release events
      Inverse modelling to retrieve the amount in time of each isotope released
  Constraints on the isotopic composition
Dose rate measurements inversion : the method

## Slide 10
10
    Measurements: Extraction of the dose rate signal when the plume blew over the station
Observed dose rate
Plume component
Ingredients of the reconstruction: step 1
Step 1: Inverse modelling to assess the timing of the release events
Notes: 10

## Slide 11
11
Results of the 1st Step: potential periods of release are identified
  Inversion to assess the timing of the release events of one isotope (Xe-133 in order to have no deposition).
    Measurements: dose rate due to the plume component
    Cost function to minimize:
Inverse
modelling
Plume extraction
Potential release periods
Ingredients of the reconstruction: step 1
Notes: 11

## Slide 12
12
Step 2: Inverse modelling to assess the source term of the 7 main isotopes
Measurements: the complete dose rate signal
It is required that the release events are among the periods identified by the 1st step of the method
Soft constraints on isotopic ratio are imposed:
The cost function to minimize use a barrier function in order to enforce the constraints
Dose rate measurements inversion
Barrier function
Notes: 12

## Slide 13
13
Reconstruction of the Fukushima-Daiichi source term
Comparisons with other ST
Cs-137 Inversed ST
Model to data comparisons
(dose rate - plume component)
Observations
ldX simulations
Notes: 13

## Slide 14
14
Reconstruction of the Fukushima-Daiichi source term
Cs-137 Inversed ST
Cs-137 Mathieu et al 2012
Cs-137 Stohl et al 2012
Comparisons with other ST
Good consistency between the different ST
Discrepancies due to uncertainties because of inaccurate meteorological forcing (precipitation, wind direct)
Model to data comparison : good agreement
Model to data comparisons
(dose rate - plume component)
Observations
ldX simulations
Mathieu et al 2012 Elements
Stohl et al 2012 Atmos.Chem.Phys.
Chino et al 2011 JNST
Winiarek et al 2012 JGR
Notes: 14

## Slide 15
15
Reconstruction of the Fukushima source term
Good agreement between model and observations
Additional releases are identified with the inverse modelling method
Discrepancies are due mainly to inaccurate meteorological forcing (precipitation, wind direct)
West – North West
South
West – South West
Inversed ST
Mathieu et al 2012
Dose rate observed
Notes: 15

## Slide 16
16
Reconstruction of the Fukushima source term
Deposition observed
Mathieu et al 2012
Inversed ST
Fairly good agreement between model (with inversed ST) and observations of deposition
Differences are due
  to inaccurate meteorological forcing (precipitation, wind)
  to deposition scheme
Comparisons with observations
Good agreement
Under estimation
Under estimation
Under estimation
Notes: 16

## Slide 17
17
Reliable inversed modelling method to assess the source term by using dose rate observations
Performances
  Good results achieved on the Fukushima accident.
  The quality of the meteorological forecast is a key point to retrieve a realistic source term.
  The reconstruction of the isotopic composition is still tricky.
Perspectives
  Improve the reconstruction of the isotopic composition: air concentration, deposition and dose rate observations
  Extend the method to all spatial scales
Use
  The method proved to be perfectly suited to crisis management
  Efficient tool to improve the understanding of an accident
Conclusions & Perspectives
Notes: 17

## Slide 18
18
Questions ?
Notes: 18